## Slide 1: Reimagining Urban Neighborhoods: Partnerships to Reuse Vacant Land in Support of Sustainable Redevelopment
St. Louis
Laura Ginn Project Manager, Green City Coalition (City + MO Dept. of Cons.)
Doug Bisson Community Planning & Urban Design Lead, HDR
Columbus
John Turner Administrator, City of Columbus Land Redevelopment Division
Reza Reyazi Asst. Admin., City of Columbus Land Redevelopment Division

## Slide 2: DATA + community
Combining Data-Driven Solutions with Community Knowledge & Priorities to Reimagine Vacancy in St. Louis
Laura Ginn, Green City Coalition Project Manager

## Slide 3: context

## Slide 4
Vacancy in St. louis
~ 7,500 Buildings & ~12,000 Lots
out of ~130,000 parcels (15%)
North City (Delmar Divide): 30% of parcels are vacant
South & Central City: 3% of parcels are vacant
Land Reutilization Authority (LRA)
nation’s oldest land bank
owns about half of all vacant properties
1,886 owned more than 30 years
average ownership tenure: 16 years
2017: 37 acres in / 63 acres out
Privately-Owned Vacancy
primarily buildings
typically end up in the land bank

## Slide 5
Vacancy in St. louis
Efforts to Address Vacancy in St. Louis
CCP Vacancy Report 2016
Land Bank Assessment 2017
New Hire: Vacancy Strategist
Mayor’s Office of Resilience – 100RC
Vacancy Collaborative
Neighborhood Vacancy Initiative
Increasing Demolition Program
Vacant Properties Portal
Green City Coalition
Urban Greening Program

## Slide 6
Green city coalition
A coalition of organizations, government offices, and neighborhoods working to convert vacancy to vibrancy in North St. Louis – anchored in a formal partnership between the City of St. Louis and Missouri Department of Conservation.
Programs Include:
Summer youth employment program – Outdoor Youth Corps
Community green space design and implementation
Implementation of Urban Greening Program demolitions, through data-driven prioritization and community-based planning
Improving demolition standards
Deconstruction program development
Nature-based programming and events
Community art projects in vacant spaces
Vacancy data transparency
Land trust feasibility study & research

## Slide 7
Urban greening program
EPA-mandated consent decree to remove impervious surface and reduce combined sewer overflows
Agreement between MSD and SLDC to spend up to $13.5 million on the demolition of vacant and abandoned buildings, and place deed restrictions on parcels (amount of stormwater absorbed by parcel cannot be reduced)
$13.5 million = ~1,200 buildings
WORKING GROUP MEMBERS
St. Louis Development Corporation
Land Reutilization Authority
City Planning & Urban Design Agency
City Building Division
Mayor’s Office of Resilience
Missouri Department of Conservation
demolitions
171
completed or approved & pending
impervious acres removed
5.93

## Slide 8: Data-driven prioritization

## Slide 9
Vacancy demolition
prioritization model
Developed to identify areas of concentrated vacancy where the removal of impervious surface and application of deed restrictions should be focused.
GOALS
Determine ideal locations for the removal of impervious surface, and
The conversion of vacant land to permanent green spaces, with a
Lean toward connecting existing green spaces, and/or filling in nature equity gaps, and an
Emphasis on ideal locations for green infrastructure.
Not just about taking a building down – about creating opportunity.

## Slide 10
Vacancy demolition
prioritization model
Find all vacant parcels
Aggregate parcels > Vacancy Clusters
Score clusters on
  Size of the vacancy cluster
  Distance to historic hydrology (MSD trunk sewer lines)
  Distance to hydrologic flow paths (current)
  Distance from major roads and highways
  Potential to connect existing green spaces
Rank clusters
Top 25th Percentile = High Priority
Present High Priority Areas to Community Members for Refinement and Green Space Planning

## Slide 11
Vacancy demolition
prioritization model
SCORE | SIZE | HYDROLOGY | SEWER | ROADS | CONNECTIVITY
Input | Cluster Only | LiDAR 2011  DEM  Flow Direction  Flow Accumulation  Polylines [con > 50k] | Remove Sewer Lines ≥ 48” wide | City of St. Louis Major Roads and Highways | Green Spaces (parks, cemeteries, gardens more than ½ acre) & Vacant Parcels  Linkage Mapper1
Process | Calculate Size | Euclidian Distance for 10’ x 10’ raster  Polygon received value of highest grid cell within |  |  | 
Normalize 0-10 Scale | Score = 10 (x-min / range) [high outliers removed first and assigned value of 10] |  |  |  | 
Final Score | Size + Hydrology + Sewer + Roads + Connectivity Total Possible: 50 // Actual Range 4.76 - 42.80 |  |  |  | 
methods
1McRae, BH & DM Kavanagh (2011). Linkage Mapper Connectivity Analysis Software. The Nature Conservancy, Seattle WA.

## Slide 12
> 20,000 Vacant Parcels
(>2,000 acres)
▼
5,605 Vacancy Clusters
▼
476 High Priority Clusters
(231 acres)
Vacancy demolition
prioritization model
application

## Slide 13: Participatory mapping

## Slide 15
From high priority areas to planning areas
High Priority Areas (top 25th percentile) become Eligible for UGP demolition funds
Mapping exercises focus on:
Neighborhood Assets
Neighborhood Opportunities
Neighborhood Challenges
Residents are asked to outline blocks where demolitions should focus and where community green space would be most desired
Areas where majority of residents agree, and where those agreements overlap with model-determined high priority areas, become the Green Space Focus Area

## Slide 16: Merging the two

## Slide 17
NORTHWEST
WALBRIDGE
ASPIRE / JUBILEE
ST. MATTHEWS
WALNUT PARK
FLORISSANT
Schools & Churches
Parks
LRA Parcels
Private Vacant Parcels
Vacant Building
Library

## Slide 18
Eligible Area and Highest Priority Vacancy Clusters

## Slide 19
Eligible for Urban Greening Program Demolition Funds & Green Space Conversion
Highest Priority Vacancy Clusters
Identified by
One Table
Identified by
Two Tables
Identified by
All Three Tables
Identified at Northwest Academy of Law
Youth Workshop
Putting It All Together

## Slide 20
Putting It All Together

## Slide 21: Green Space Focus Area the proposed area to be converted to green space amenity(ies); identified by computer modeling AND residents
Demolition of ALL LRA buildings
HOLDS on ALL LRA lots
Potential Demolition of Privately-Owned Vacant & Abandoned Buildings that are Structurally Condemned
Planning for Green Spaces
Deed Restrictions on Vacant Parcels

## Slide 22: Green Space Adjacent Area blocks surrounding the Green Space Focus Area; primed for redevelopment and infill housing
Assessment of all LRA buildings prior to demolition
City & Partners work to implement redevelopment toolkit (incentives, community benefit agreements, support programs…)

## Slide 23: School Zones: High Risk Area within 500 feet of a School’s parcel boundary

## Slide 24: School Zones: High Risk Area within 500 feet of a School’s parcel boundary
Assessment of all LRA buildings prior to demolition

## Slide 25
Green Space
Focus Area
Green Space
Adjacent Area
School Zones:
High Risk Area

## Slide 26
Proposed Demolitions
LRA Buildings
Green Space
Focus Area
28
Green Space
Adjacent Area
45
Following Review
School Zone
53
126
Immediate

## Slide 27: Wells goodfellow

## Slide 28
Neighborhood context

## Slide 29
Wells goodfellow planning efforts
Neighborhood Planning Workshops Aug-Nov 2016
Kansas State University Technical Assistance for
Brownfields (EPA) > SKEO Solutions
Community Advisory Committee meets quarterly
Community Events ~6 / year
- beautification / planting projects
- trash sweeps / clean ups
- invasive species removal
- nature-based field trips
77 demolitions; 35 in green space focus area
Xtreme LA Design Challenge
landscape architecture design challenge hosted by
Washington University in St. Louis – urban water focus
Green Space Design Charrette
KSU TAB (EPA) > HDR/CSRA to develop
design renderings for neighborhood green space

## Slide 30: Wells goodfellow
NEIGHBORHOOD GREENSPACE PROJECT
Doug Bisson, Community Planning and Urban
Design Lead, HDR

## Slide 31: EXISTING CONDITIONS

## Slide 33: CHARRETTE PROCESS

## Slide 36: REFINED CONCEPT

## Slide 37
REFERENCE IMAGES
PLAN VIEW

## Slide 38: PERSPECTIVE RENDERING GOODFELLOW GATEWAY

## Slide 39: VACANT LOT RETROFIT

## Slide 43
excavations

## Slide 44: NEXT STEPS
ROBERT J TRULASKE FAMILY FOUNDATION GRANT
+ NATIONAL FISH & WILDLIFE FOUNDATION GRANT
+ MISSOURI DEPARTMENT OF CONSERVATION COST-SHARE
= EXCAVATION, REGRADING, AND SEEDING FALL/WINTER 2018